## Slide 1
Benchmark Report on Couchbase Load Testing
Performance Evaluation of Key-Value Operations
Daniel Kleyman
October 2024

## Slide 2
Introduction
Purpose of the Report:
This report provides a comprehensive overview of the benchmarking process conducted to evaluate Couchbase's key-value functionality.
Objective of Testing:
As part of the selection process for an enterprise caching solution, the objective is to develop a load testing strategy to benchmark the key-value functionality of Couchbase.

## Slide 3
Couchbase Setup and Load Testing Methodology
1. Couchbase Setup:
• Installation: The Couchbase instance was set up using Docker with default settings.
• Bucket Configuration: A bucket named 'loadtest' was created for testing.
2. Load Testing Methodology:
• Multi-threaded Java Application: Each thread uploads a JSON file and retrieves it.
• Test Duration: The load tests were executed for 3 minutes.
• Operations Performed: Each thread performed one upload followed by three retrieve operations of the uploaded file by key.
3. Monitoring:
• Metrics Collection: Micrometer was used to collect application performance metrics.
• Metrics Storage: Prometheus was utilized for storing the collected metrics.
Report generated using Apache POI.

## Slide 4
Test Scenarios for Couchbase Load Testing
1. Overview of Test Scenarios:
• Purpose: To benchmark Couchbase's key-value functionality under various conditions.
2. Scenario Types:
• Thread Pool Scenarios: Tests varying the number of threads used for load operations from 5 to 15, use 2 JSON files of different sizes (1 kb and 25 kb), write to unique or shared keys and use Couchbase default connection pool size.
• Connection Pool Scenarios: Tests evaluating performance with a fixed number of threads (10), use JSON files of same size (25 kb), unique keys, connection pool size vary from 5 to 15.

## Slide 5
Specific Scenarios
Scenario 1: 5 threads, 25 kb JSON, unique keys.
Scenario 2: 5 threads, 25 kb JSON, shared key.
Scenario 3: 10 threads, 25 kb JSON, unique keys.
Scenario 4: 10 threads, 25 kb JSON, shared key.
Scenario 5: 15 threads, 25 kb JSON, unique keys.
Scenario 6: 15 threads, 25 kb JSON, shared key.
Scenario 7: 5 threads, 1 kb JSON, unique keys.
Scenario 8: 5 threads, 1 kb JSON, shared key.
Scenario 9: 10 threads, 1 kb JSON, unique keys.
Scenario 10: 10 threads, 1 kb JSON, shared key.
Scenario 11: 15 threads, 1 kb JSON, unique keys.
Scenario 12: 15 threads, 1 kb JSON, shared key.
Scenario 13: 10 threads, 25 kb JSON, unique key, connection pool size 5.
Scenario 14: 10 threads, 25 kb JSON, unique key, connection pool size 10.
Scenario 15: 15 threads, 25 kb JSON, unique key, connection pool size 15.

## Slide 6
Results Overview
This section provides an overview of the performance metrics observed during the Couchbase load testing.
Key Performance Metrics:
• Average Latency of PUT Operations: Average latency measured in milliseconds.
• Average Latency of GET Operations: Average latency measured in milliseconds.
• Overall Average Response Time: Overall average response time measured in milliseconds.
• Transactions Per Second (TPS): Total successful transactions processed per second.
• Total Error Rate: Total error rate observed during the testing phase in percentage.
• Total Number of Successful Operations: Total successful operations executed.
These metrics provide insights into Couchbase's performance under load and areas for potential optimization.

## Slide 7
Thread Pool Tests Results
Scenario ID | Total Successful Operations | Total Error Rate (%) | Transactions Per Second (TPS) | Average PUT Latency (ms) | Average GET Latency (ms) | Overall Average Response Time (ms)
Scenario 1: threads=5,25kb,unique keys | 225796.0 | 0.00 | 251.20 | 4.90 | 3.70 | 4.00
Scenario 2: threads=5,25kb,shared key | 288408.0 | 0.00 | 320.70 | 3.90 | 2.90 | 3.10
Scenario 3: threads=10,25kb,unique keys | 337672.0 | 0.00 | 187.70 | 6.70 | 4.90 | 5.30
Scenario 4: threads=10,25kb,shared key | 403472.0 | 0.00 | 224.20 | 5.60 | 4.10 | 4.50
Scenario 5: threads=15,25kb,unique keys | 435624.0 | 0.00 | 161.40 | 7.70 | 5.70 | 6.20
Scenario 6: threads=15,25kb,shared key | 481700.0 | 0.00 | 178.40 | 7.00 | 5.10 | 5.60
Scenario 7: threads=5,1kb,unique keys | 573940.0 | 0.00 | 638.20 | 1.70 | 1.50 | 1.60
Scenario 8: threads=5,1kb,shared key | 604440.0 | 0.00 | 672.00 | 1.60 | 1.50 | 1.50
Scenario 9: threads=10,1kb,unique keys | 935356.0 | 0.00 | 519.90 | 2.00 | 1.90 | 1.90
Scenario 10: threads=10,1kb,shared key | 1036100.0 | 0.00 | 575.80 | 1.80 | 1.70 | 1.70
Scenario 11: threads=15,1kb,unique keys | 1311916.0 | 0.00 | 486.10 | 2.20 | 2.00 | 2.10
Scenario 12: threads=15,1kb,shared key | 1402140.0 | 0.00 | 519.50 | 2.00 | 1.90 | 1.90

## Slide 8
Connection Pool Tests Results
Scenario ID | Total Successful Operations | Total Error Rate (%) | Transactions Per Second (TPS) | Average PUT Latency (ms) | Average GET Latency (ms) | Overall Average Response Time (ms)
Scenario 13: connections = 5 threads =10 | 351116.0 | 0.00 | 195.10 | 6.70 | 4.60 | 5.10
Scenario 14: connections = 10 threads =10 | 344472.0 | 0.00 | 191.40 | 6.80 | 4.70 | 5.20
Scenario 15: connections = 15 threads =10 | 330048.0 | 0.00 | 183.40 | 6.90 | 5.00 | 5.50

## Slide 9
Findings, Suggestions and Conclusion
Findings:
• Total Successful Operations: High counts in scenarios with more threads and smaller JSON sizes.
• Transactions Per Second (TPS): The highest TPS was observed in scenarios with 5 threads and smaller payloads.
• Shared vs. Unique Keys: Using shared keys resulted in better TPS in many scenarios, suggesting that caching mechanisms or key distribution may play a role in performance.
• Performance Bottlenecks: A significant drop in TPS was noted at 15 threads with larger JSON sizes (25 KB), indicating a threshold where resource constraints begin to limit performance.
• Diminishing Returns: A decline in TPS was evident when exceeding 5 threads, suggesting Couchbase may have optimal operating limits under the tested conditions.
• Data size: Payload size greatly affects latency, with 25 KB causing significant increases in PUT and GET latencies compared to 1 KB, which had minimal impact.
• Connection pool size: Predefined connection pool sizes showed minimal impact on database performance.
Suggestions for Further Testing:
• CPU Utilization, Memory Usage, Disk I/O Performance, Network Latency and Throughput, Couchbase Performance Metrics.
Conclusion:
Higher thread pool sizes generally increased the total successful operations, especially with smaller JSON payloads. However, beyond 5 threads, TPS began to decline, particularly for larger payloads, indicating diminishing returns due to resource contention. Therefore, optimal thread pool size is crucial to balance performance and latency, necessitating careful tuning based on workload characteristics.

## Slide 10
THANK YOU FOR YOUR ATTENTION!